INTERNATIONAL ELECTROTECHNICAL COMMISSION SYSTEM FOR CERTIFICATION TO STANDARDS RELATING TO EQUIPMENT FOR USE IN EXPLOSIVE ATMOSPHERES (IECEx SYSTEM)

# TITLE: Proposed Decision Sheet to clarify use of IEC 60079-28 for various light sources

# Circulated to: ExTAG – IECEx Testing and Assessment Group

INTRODUCTION

This document contains a proposed Decision Sheet arising from discussions at the 2016 ExTAG Training session held in Umhlanga and is submitted for discussion/approval at the 2016 ExTAG Technical meeting.

IECEx Secretariat

Julien Gauthier

ExTAG Secretary

| Address: IECEx Secretariat Level 33 Australia Square 264 George Street Sydney NSW 2000 Australia Web: www.iecex.com | ExTAG Secretary Mr Julien Gauthier LCIE S.A. 33 Avenue du General Leclerc 92260 Fontenay-aux-Roses FRANCE Tel: +33 1 40 95 55 26 Fax: +33 1 40 95 89 37 Email : julien.gauthier@fr.bureauveritas.com |
| --- | --- |

Draft (in principle) for text for an ExTAG DS in dealing with luminaires concerning whether or not IEC 60079-28 needing to be invoked

Background:

Following circulation of ExTAG/409/CD and the related comments document ExTAG/431/CC, and a presentation by Xu Jiang Ping at the ExTAG Training Workshop on 5 September 2016, a general discussion was held regarding how to resolve many issues concerning the use and non-use of IEC 60079-28 for luminaires.

Maintenance Team MT60079-28 has currently no convenor and we await feedback from the MT regarding some of these questions.

It was noted that the use of IEC 60079-28 will be made mandatory in the draft text for the next edition of IEC 60079-0, about to be released as a FDIS, but market confusion exists today and an interim solution is required, as well as a decision on how IECEx will implement the new requirement once the standard is published.

Question:

How can the market place be given confidence that the ExCB has performed the Ignition Hazard Assessment described in Annex C of IEC 60079-28 and that a proper technical decision has been taken as to whether or not the standard applies to a particular LED Luminaire?

Answer:

For all LED Luminaires (with the exception of those of EPL Gc or Dc which are specifically exempted from the scope of the standard) the IECEx Certificate shall either clearly show that IEC 60079-28 is included in the certification (by listing on the front page) or , if appropriate, the equipment description shall include the following statement:

This luminaire has been subjected to the Ignition Hazard Assessment required by Annex C of IEC 60079-28 and found to be out of scope of that standard.  Details of this assessment are included in the IECEx Test Report.

Supplementary information:

ExCBs/ExTLs which do not have IEC 60079-28 in their IECEx scope are required to prove that they have sufficient understanding of the standard in order to be able to make that judgement.  With the new edition of IEC 60079-0, this will be recorded in the TCD at the calling clause for the potential use of IEC 60079-28.  Until the appropriate TCD is available, the assessor will record this at ????