### INTERNATIONAL ELECTROTECHNICAL COMMISSION (IEC) SYSTEM FOR CERTIFICATION TO STANDARDS RELATING TO EQUIPMENT FOR USE IN EXPLOSIVE ATMOSPHERES (IECEx SYSTEM)

TITLE: Revised Draft ExTAG Decision Sheet – Location of Electrostatic Discharge Hazard Warning

# Circulated to: ExTAG – IECEx Testing and Assessment Group

INTRODUCTION

This document, ExTAG/458A/CD Draft ExTAG Decision Sheet – Location of Electrostatic Discharge Hazard Warning was prepared by UL LLC and circulated to ExTAG for comment.  The Compilation of Comments, along with observations from the originator, are contained in ExTAG/483/CC.

This updated version, ExTAG/458A/CD Draft ExTAG Decision Sheet – Location of Electrostatic Discharge Hazard Warning takes into account the comments received and is issued for final discussion during the 2017 ExTAG Washington meeting.

Julien Gauthier

Julien Gauthier

ExTAG Secretary

| Address: IECEx Secretariat Level 33 Australia Square 264 George Street Sydney NSW 2000 Australia Web: www.iecex.com | ExTAG Secretary Mr Julien Gauthier LCIE S.A. 33 Avenue du General Leclerc 92260 Fontenay-aux-Roses FRANCE Tel: +33 1 40 95 55 26 Fax: +33 1 40 95 89 37 Email : julien.gauthier@fr.bureauveritas.com |
| --- | --- |

IECEx / ExTAG DECISION

| Standard: IEC 60079-0 (Ed 6) | Clause: 7.4.2 e), 29.12 g) | Date: 2017 07 Originator of proposal: UL |
| --- | --- | --- |
| Subject: Location of Electrostatic Discharge Hazard Warning Status of document: | Key words: Electrostatic discharge Warning marking | TC/SC involved: IEC/TC31 WG 22 Draft Decision Sheet: ExTAG/458A/CD |
| Background For fixed installations, where the installation is intended to minimize the risk from electrostatic discharge, there is a requirement for 1) an “X” condition marking, 2) instructions that provide guidance for the user to minimize the risk from electrostatic discharge, and 3) a warning marking that reads, “WARNING – POTENTIAL ELECTROSTATIC CHARGING HAZARD – SEE INSTRUCTIONS”, or equivalent. When applying this requirement for IECEx equipment certifications, inconsistencies have been encountered as to how ExCBs/ExTLs have been applying the third element of the requirement regarding the warning marking. The most significant inconsistency has been regarding the required location for the warning marking. Question Regarding the required location of the marking, “WARNING – POTENTIAL ELECTROSTATIC CHARGING HAZARD – SEE INSTRUCTIONS”, does the marking have to be visible to the operator of the equipment after installation, or is it permitted that the marking only be visible to the user/installer during installation? An example of the latter location for the marking would be on the rear of a panel-mounted computer. Answer If the operator is required to take action(s) after installation in order to maintain the required level of safety, the marking must be in a location likely to be visible to the operator after installation.. If the operator is required to interact with the equipment during use, this marking is to be in proximity to the surface of concern from being interacted with, as the marking is critical for the operator at the part of the equipment subject to the risk. |