### INTERNATIONAL ELECTROTECHNICAL COMMISSION (IEC) SYSTEM FOR CERTIFICATION TO STANDARDS RELATING TO EQUIPMENT FOR USE IN EXPLOSIVE ATMOSPHERES (IECEx SYSTEM)

TITLE: Draft ExTAG Decision Sheet - Brazing and welding of flameproof enclosures.

# Circulated to: ExTAG – IECEx Testing and Assessment Group

INTRODUCTION

Document ExTAG/350/CD, was prepared by INTERTEK, US, with the involvement of IEC TC 31 MT 60079-1. A revised version of this document ExTAG/350A/CD, has been prepared taking into account comments received and is submitted for consideration by ExTAG.

Comments received were collated in document ExTAG/358/CC.

This document is now submitted for final comment, prior to forwarding for publication.  Please advise if you have any objections to this draft being published no later than 2015 04 07 to the ExTAG Secretary, Mr. Julien Gauthier, via

Christine Kane

Julien Gauthier

ExTAG Secretary

| Address: IECEx Secretariat Level 33 Australia Square 264 George Street Sydney NSW 2000 Australia Web: www.iecex.com E-mail: info@iecex.com | ExTAG Secretary Mr Julien Gauthier LCIE S.A. 33 Avenue du General Leclerc 92260 Fontenay-aux-Roses - FRANCE Tel: +33 1 40 95 55 26 Fax: +33 1 40 95 89 37 Email : julien.gauthier@fr.bureauveritas.com |
| --- | --- |

| Member Body | Clause/ Sub-clause | Paragraph Figure/ Table | Type of comment General/ technical/ editorial | COMMENTS | Proposed change | Observation |
| --- | --- | --- | --- | --- | --- | --- |

COLLECTION OF IECEx / ExTAG DECISION

| Standard: IEC 60079-1 Ed. 7 (2014) IEC 60079-1 Ed. 6 (2007) | Clause: 3.3, 6.1, 16.2, 16.3 (Ed. 7) 3.3, 6.1, 16.2 (Ed. 6) |  |
| --- | --- | --- |
| Subject: Enclosures welded or brazed together Status of document: DRAFT | Key words: Welding, brazing, joint, enclosure | Date: 2014-11-21 Rev. 2015-01-27 Originator of proposal: Intertek (US) TC/SC involved: TC 31 MT 60079-1 |
| Title: Brazing and welding of flameproof enclosures. Background: Some flameproof enclosures are made from multiple pieces that have been welded together, due to size. Some enclosures are made from multiple pieces that have been brazed together, for the same reason. Although neither IEC 60079-0 nor IEC 60079-1 defines welding or brazing, both practices are generally understood. IEC 60079-1 does have some provisions for welding (16.2 in Ed. 6, 16.2 and 16.3 in Ed. 7). There is some doubt as to whether an enclosure that is formed by brazing constitutes a “welded enclosure”, or if brazing makes an enclosure with a cemented joint. The primary argument for considering a brazed connection a cemented joint is that it uses other than native material (e.g., other than steel), creating an alloy of two other metals that completely fills the gap between the two pieces being brazed. The definition of flameproof joint in 3.3 does not lead to a clear answer, as both welded and brazed joining of enclosure parts would meet the definition of a flameproof joint. Question 1: Is an enclosure section made up by welding pieces together considered a single enclosure section, or two sections with a flameproof joint? Question 2: Is an enclosure section made up by brazing pieces together considered a single enclosure section, or two sections with a flameproof joint? Answer: Question 1: A welded enclosure section is a single section, subject to the applicable type tests and routine tests. Question 2: A brazed enclosure section remains two sections, joined by a flameproof joint, subject to the applicable type tests and routine tests. Brazed joints need not be subjected to the thermal endurance testing specified in IEC 60079-0. |