Record of IECEx / ExTAG Decisions

| Standard: IEC 60079-11 | Clause: | Sheet No. |
| --- | --- | --- |
| Subject: Limitation of RF power Status of document: Approved | Key words: RF Power limitation | Decision of meeting Date: Originator of proposal: CN/NEPSI TC/SC involved: SC31G |
| Question: RF (10 kHz to 3000 GHz) radiation energy is commonly recognized as a potential ignition source. How should the limitation of RF radiation power be applied for the assessment and certification of RF apparatus (intrinsically safe as a whole or at least for the RF output) used in explosive atmospheres? Answer: The following limitation values of RF radiation power should be used for the assessment and certification of RF apparatus used in explosive atmospheres, considering applicable fault conditions for 'ia' and 'ib' respectively: For Group IIA: 6W maximum; For Group IIB: 4W maximum; For Group IIC: 2W maximum. Note: The listed data are extracted from national standards and European technical reports. |